## Slide 1: Introduction to microcontrollers
Experiment-4
Microprocessors
Microcontrollers

## Slide 2: Microprocessors
Microprocessors run programs
Implicit characteristics:
Can read program stored in memory
Can understand instructions embedded within programs
Can interpret and execute these instructions
Carry out arithmetic and logic operations
Read input devices: keyboard/mouse…..
Send output: computer screen/printer……
Exchange information with external devices (network communication)

## Slide 3: Computer program
Computer programs contain instructions
e.g. x = y + z;
Instructions contain operations and operands
  Here ‘+’ is the operation,
  And ‘y’ and ‘z’ are the operands
Many instructions read/write data(operands) from/to memory
  (e.g. read y & z, and write back the value ‘x’)
Data is written to RAM
Data may be read from RAM or ROM

## Slide 4: Microprocessor essentials
ROM having stored program
An instruction set (specific to mP)
Microcode which interprets the instruction code
An arithmetic and Logic unit to carry out instructions
A scratch pad(set of registers)
Hardware features to read from, and write to memory
Facility to interface with the external world
(Input and Output ports)
React to external events, stimuli
Count external events/generate delays
(timers and counters)
(Interrupts)

## Slide 5: Microprocessor
Microprocessor
comprises of
CPU
  ALU
  Register file
  I/O
  Interrupts
  Busses
CPU
ALU
I/O
BUS
Int

## Slide 6: Microprocessor system
CPU
ALU
I/O
Int
CPU
RAM
ROM
Interrupts
Peripherals
  I/O ports
  Timers
  Counters
  Serial port
RAM
Peripherals
ROM
BUS

## Slide 7: Microcontroller
Microcontrollers combine all
mp components in a single chip
CPU
RAM/ROM/Registers
I/O ports
Peripherals
Interrupts
CPU
ALU
I/O
Int
RAM
ROM
Registers
Peripherals

## Slide 8: Microcontroller architecture
Memory
  RAM
  Flash ROM
I/O ports
Memory architecture
See link for detailed
8051 uC architecture
CPU
ALU
UART
Int
RAM
ROM
Registers
Counter/timer
I/O
D0
D1
D2
D3
D4
D5
D6
D7
I/O
D0
D1
D2
D3
D4
D5
D6
D7
I/O
D0
D1
D2
D3
D4
D5
D6
D7
I/O
D0
D1
D2
D3
D4
D5
D6
D7
http://www.met.iitb.ac.in/~nkk/NKK/8052_architecture.pdf

## Slide 9: 8051 microcontroller
8 bit ALU (works on 8 bit operands)
64K ROM, 256 byte RAM, 4x8 bit register files
Provides two external interrupts
I/O ports (parallel (4 x 8bit) and one serial (UART))
Three 16bit multifunction timers and counters
Arithmetic instructions (integer operands)+ , - , x , ¸
Logic instructions AND, OR, XOR, NOT, SHIFT, ROTATE
Memory Read/Write instructions
Code branching instructions
Ability to call and execute subroutines

## Slide 10: More about registers and ports
ALU
I/O
Int
RAM
ROM
Register file
Peripherals
0
1
2
3
4
5
6
7
D0
D1
D2
D3
D4
D5
D6
D7
Registers are storage locations. In 8051 mC, registers store 8 binary bits organized as a byte
Data stored in RAM, ROM and Registers can be presented on any port
Bit position D0 is presented on port line ‘0’, D1 in port line ‘1’ and so on
Ports can be INPUT or OUTPUT
D7
D6
D5
D4
D3
D2
D1
D0
Register or Memory
Parallel Port
R0
R1
R3
Rn
CPU
R0

## Slide 11: LEDs connected on P0 & P1
Ports are given an
Identity(P0,P1,P2..)
Each port has 8 pins
Each Pin has an
Identity(P0.1,P0.2...)
Observe LEDs on ports
Output High on a port
pin to light a LED
P89C51
P0.0
P0.1
P0.2
P0.3
P0.4
P0.5
P0.6
P0.7
LD1
LD2
LD3
LD8
LD7
LD6
LD5
LD4
+5v
R29
R28
R35
R34
R33
R30
R32
R31
Schematic diagram of the 8 LEDs connected to port 0
P
O
R
T
0
7
6
5
4
3
2
1
0

## Slide 12: Timers and counters
8051 provides three 16 bit counters
Counters can be used to count pulses
Or generate precise delays
GATE
INT1
TR1
T1 PIN
C/T = 0
C/T = 1
Control
TL1
8bits
TH1
8bits
TF1
interrupt
12MHz clock
¸ 12
1Mhz
Timer 0/1 in mode-1

## Slide 13: Timer 0/1 in Mode-2: Auto reload
Used to generate baud rate for serial communication

## Slide 14: Memory architecture
Four memory spaces
Special function
registers
64K Ext Data memory
64K program memory
0
64K
0
128 byte IRAM
128
128 byte
SFR RAM
256
128 byte ERAM
INTERNAL
4/8K

## Slide 15: Special function registers
Special function registers are used to configure peripherals.
Parallel I/O ports are mapped as SFR
Timer modes are configured through SFR
Serial port is operated through SFR
Interrupts are controlled through SFR
mC programming most often requires setting SFRs to configure and use peripheral devices

## Slide 16: Examples of SFR
I/O Ports: P0, P1, P2 & P3
Timer mode set register: TMOD
Timer Control register: TCON
Timer-0/Timer-1 LSB register TL0/TL1
Timer-0/Timer-1 MSB register TM0/TM1
Accumulator/B register: ACC/B
Interrupt enable/priority register: IE/IP
Serial port registers: SCON, SBUF
Program status register: PSW
Data pointer registers: DPH/DPL

## Slide 17: More on SFRs
SFR are 8 bit registers
Some 8 bit SFRs also have bit significance
TCON
PORT-2
P2.7
P2.6
P2.5
P2.4
P2.3
P2.2
P2.1
P2.0

## Slide 18: Interrupts
mC reacts to external world through
  Polling I/O lines
  Interrupts (mC may have multiple interrupts)
Interrupts initiate Interrupt Service Routines
Interrupts can be external to mC or generated by internal events such as ‘timer overflow’
Interrupts are associated with priority and vector addresses
Concurrent interrupts are resolved through an interrupt priority mechanism

## Slide 19: More on ports
All 8051 ports can be used for input or output
A port pin can be made Low or high
  Low value is signalled by logic level =0 , usually Voltages below 0.4V
  High value is signalled by logic level=1 (voltage >2.4V)
All port pins can be read (like reading from memory)
To read logic status of a port pin, Logic level ‘1’ first, logic ‘1’ has to be outputted on that Pin
E.g. to read port P1 pins, two steps are needed.
  P1  0xFF
  Register R0  P1

## Slide 20: Using the microprocessor Kit
microcontroller
Port P2
As out put
Port P2
As input
Port P0
I/O port
Thermocouple amplifier
Temperature sensors
DAC
ADC
Serial port

## Slide 21: Using microcontroller kit
Using the Keil IDE to write C-code and cross-compile it.
Compiled code can be tested on PC by using Keil debugger
Download compiled code(Intel-hex format) to microcontroller by employing serial loading feature
Run code on target CPU and debug errors

## Slide 22: Experiment-4
Using an IDE and cross compiler
Writing a C program
Compiling
Downloading
Run & Debug
Understanding special function registers {SFR}
Using microcontroller ports {Architecture}
Using microcontroller timer {Architecture}

## Slide 23: Structure of mC C-code
Describe briefly, what the program does or achieves in the header.
/***************************************/ .. …Comments
#include <reg52.h> /* Typical include files in C language */
#define ………. /* include your define statements here */
sbit …… /*include your SFR bit definitions here */
int…. /* include global variable definitions here */
char ….
Void func1 () /* include your functions here/*
  {
  }
void main () /* main code */
{
/* include your comments in the main program*/
}

## Slide 24: Using the IDE and cross compiler
Run the IDE (Keil software)
Create the Code as .C file through Keil IDE
Create a project in Keil IDE
Associate your .C file with the project
Add a mandatory ‘startup code’ file
Compile the C code into
Run compiled code in the debugger provided by Keil IDE
Debugger provides dummy ports to check and confirm port operations

## Slide 25: Experiment-4.1
Assign a value to Port 2 in your program, execute the program and observe the value on Port 2 LEDs.
Code>
#include <REG52.H> /* special function register declarations */
/* for the intended 8051 derivative */
#include <stdio.h> /* prototype declarations for I/O functions */
void main (void)
{
while(1) //End less while so that program never ends
{
P2 = 0x55;
}
}

## Slide 26: Experiment-4.3
Give input at port 0 using jumpers J2 to J9. Write a program to assign this value to Port 2
Note: A connected jumper assigns bit value ‘1’ to the micro-controller pin.
Solution:
#include <REG52.H>
#include <stdio.h>
void main (void)
{ P0=0xFF; //assigns bit value ‘1’ to the micro-controller pin.
//0xFF or 1111111 or 255
while(1) //End less while so that program never ends
{ P2 = ~P0;} //inverter (~)
} }

## Slide 27: Timer delays: generating delay of 1ms
Initialize Port 2 with the value 00h.
After a delay of 1 ms assign Port 2 the value FFhex.
After a delay of 1 ms assign Port 2 the value 00hex.
Run step 2 and step 3 in an infinite loop.
This should generate a square wave on the pins of Port 2.
For generating the delay you need to use a timer.
What is the frequency?

## Slide 28: Delay generated by software
#include <REG52.H>
#include <stdio.h>
void softwaredelay (unsigned int x)
{
unsigned char d;
while(x-->0)
{
for (d=0;d<110;d++) {;}
}
}
void main (void)
{
//Initialize Port 2 with value 00h. P2=0x00;
while(1)
{ P2=0xFF;
softwaredelay(1);
P2=0x00;
softwaredelay(1);
}
}

## Slide 29: Delay generated by hardware
GATE
INT1
TR1
T1 PIN
C/T = 0
C/T = 1
Control
TL1
8bits
TH1
8bits
TF1
interrupt
11.0592Mhz
¸ 12
0.922Mhz
TMOD
0 0 0 1
Starting count= 64614
Hex of 64614 = 0xFC66
65535-64614=921
921 x 1.085x10-6 = 999.3mSec

## Slide 30: Delay generated by hardware
#include <REG52.H>
#include <stdio.h>
//delay using Timer0
void hardwaredelay(void)
{
TMOD = 0x01; //timer0 in mode0
//values for 1msec = 0xFC66
TL0 = 0x66;
TH0 = 0xFC;
TR0 = 1; //start timer
while(TF0==0)
{;}
TR0 = 0; //stop timer
TF0 = 0;
}
void main (void)
{
P2=0x00; //Initialize Port 2 with the value 00h.
while(1)
{
P2=0xFF;
hardwaredelay();
P2=0x00;
hardwaredelay();
}
}

## Slide 31: Some interesting programs
Students are advised to write code to
Generate a running border on P0 and P2
Running border from P0  P2  P0 
Understand how to use output data to DAC and create audio output of known frequency through onboard speaker
Port P0
Port P2

## Slide 32
Read experiment-4 laboratory manual
and other associated files on moodle