## Slide 1: MM215 Experiment-5
FILTERING THROUGH PROGRAMMING
IN MODERN-DAY DATA ACQUISITION

## Slide 2: Measurements and sensors
Need to measure physical quantities
  Displacement/Velocity/accelaration
  Temperature
  Force/pressure/Load
  Flow-rate/Level of liquids and solids
  Voltage/Current/Power
  Concentration of a solution/pH/pK
Sensors are used to make such measurements

## Slide 3: Sensors and signals
Sensors and transducers
Sensors convert one engineering variable in to another. For example-
  Current  voltage
  Temperature  voltage
  Force  Resistance
Sensor
Engineering variable to be measured
Sensor output
 Voltage
Sensor output is frequently referred to as ‘signal’

## Slide 4: Sensor signals & noise
Sensors are not ideal. All sensor outputs have noise.
Thus, all engineering measurements are coloured by sensor noise
The sensor noise needs to be removed before a measurement can be meaningfully used
Sensor
Input = x(t)
y(t) ..where y(t) = f(x(t))
+ n(t) ..[random noise]

## Slide 5: Sensor noise
Sensor output usually consists of DC or AC voltage, often referred as signal.
Noise implies, existence of signal components which do not arise due to the input
As sensor input and output are functions of time, noise component is also a function of time
Noise is usually measured as noise voltage, or noise power in sensor output

## Slide 6: Sensor noise
If the sensor output is expressed in frequency domain, sensor noise can be seen as unwanted frequency components.
Frequency
Rel. Intensity
Filtration
  Low pass
  High pass
  Band pass
  Band reject
Signal
How to remove this noise
Noise has high frequency components
Noise has low frequency components
Noise is evenly spread out

## Slide 7: Filtration
Traditionally electrical and/or electronic circuits perform filtering of noise
Modern practice is to use computers for measurements and controls of engineering systems
But computers work only on discretized data often obtained through ADCs
As computers are presented with noisy data, there is a need to filter it by employing data processing techniques.

## Slide 8: Data acquisition by computers
Sampling of signals by using data acquisition systems
  Sensor  Analog signal conditioning 
  Sample & Hold  ADC  digital data 
  Digital Data Digital signal conditioning 
  Sanitised digital data  recording/display/DAC
Sampling rate requirements
Sampling theorem

## Slide 9: Sampling of data
Sampling rate

## Slide 10: Sampled data
Sampling rate

## Slide 11: Impact of sampling rate

## Slide 12: Impact of sampling rate

## Slide 13: Reconstructed waveform
Loss of information due to low sampling rate

## Slide 14: Aliasing due to low sampling rate
Low freq.
High freq.

## Slide 15: Low pass filtering
y(k+1)= a u(k) + (1-a) y(k), 0 < a < 1
k
0 1 2 3 4 5 6 7 8 9 11 13 15 17

## Slide 16: ADC/DAC connectivity with uC
L
A
T
CH
PORT-0
mC
PORT-2
DAC
DACLATCHENABLE
DAC OUT
START
READADC
ADC
CHIPENABLE
END OF
CONVERSION
This line shared between ADC and DAC
WR
INTR
RD
CS
Making WR=0 starts a conversion and INTR becomes=1. At the end of conversion INTR becomes 0. Tying INTR with WR ensures continuous conversions.
To read converted value, make RD=0, CS=0, and read from P0.
For sending an output to DAC
Output value on P0 (make sure CS=0)
Make DACLATCHENABLE =1 and then back to 0

## Slide 17: ADC connectivity with CPU Pins
ADC
START
READADC
CHIPENABLE
END OF
CONVERSION
WR
INTR
RD
CS
L
A
T
CH
DACLATCHENABLE
(P1.5)
(P1.2)
(P1.3)
(P1.4)

## Slide 18: Steps to read ADC & display on P2
Initialization : Define port bits P1.2-5
START=READADC=1
Measure:
Wait for START to become =0
When START=0
  READADC=CHIPENABLE=0
  Configure P0 in input mode
  Read converted ADC value from P0
READADC=CHIPENABLE=1
Write data on P2
Repeat from 1
Void main(void) {
unsigned char adcdata;
While (1) {
while (START ==1){;}
READADC=0; CHIPENABLE=0;
P0=0xff;
adcdata=P0;
READADC=1;
CHIPENABLE=1;
P2=~adcdata;//P2 is inverted
} }
#include <REG52.H>
sbit DACLATCHENABLE=P1^5;
sbit START= P1^2;
sbit READADC=P1^3;
sbit CHIPENABLE=P1^4;
READADC=1;
START=1 ;

## Slide 19: Measure and filter data. Output to DAC
#include <REG52.H>
//Define ADC control pins
sbit DACLATCHENABLE=P1^5;
sbit START= P1^2;
sbit READADC=P1^3;
sbit CHIPENABLE=P1^4;
void main(void)
{ //Main loop begins here
unsigned char adcdata,
previousdata=0;
//Setup ADC control lines
DACLATCHENABLE=0;
READADC=1;
CHIPENABLE=1;
while (1) { //infinite loop begins
while (START ==1){;} //Wait for start pin to go low
READADC=0; //Setup ADC read
CHIPENABLE=0; //Pins
P0=0xff; //Set P0 in input mode
adcdata = P0; //Read data from ADC
READADC=1; //Restore ADC read
CHIPENABLE=1; //Pins
//Following line filters data
P0= ~(char) ( (float)adcdata*0.05 + (float)previousdata*0.95);
Previousdata = adcdata ;
DACLATCHENABLE=1; //send to
DACLATCHENABLE=0; //DAC
} //infinite loop ends
} //and ends here

## Slide 20: Suggested programs
Read from ADC and output read value on P2
Read from ADC and output directly to DAC and simultaneously display on P2
Read from ADC Filter data and output to DAC and simultaneously display on P2
Add the following delay function to time ADC measurements (see next slide).
Structure the program by converting read-adc routine into a function which is called from main()

## Slide 21: Suggested programs
//delay function
//call as msec(1) for 1msec delay
void msec(unsigned int x)
{unsigned char j;
while (x--> 0)
{for (j=0; j <125; j++) { ; } }}
Code example in box uses the delay routine to generate 100msec delay between subsequent measurements and send measured data to port P2
#include <REG52.H>
void msec(unsigned int); //Define prototype
sbit DACLATCHENABLE=P1^5;
sbit START= P1^2;
sbit READADC=P1^3;
sbit CHIPENABLE=P1^4;
void main(void) {
unsigned char adcdata;
While (1) {
READADC=1;
START=1 ;
while (START ==1){;}
READADC=0;
CHIPENABLE=0;
P0=0xff;
adcdata=P0;
READADC=1;
CHIPENABLE=1;
P2=~adcdata;
msec(100); //Introduce 100ms delay
} }
 Place delay routine here 

## Slide 22
Over to experiment-5 lab lecture